Lab Name:      					Procedure #:

Procedure: CLIA Complexity: WAIVED

| Prepared By | Date Adopted | Supersedes Procedure # |
| --- | --- | --- |

| Review Date | Revision Date | Signature |
| --- | --- | --- |

| Distributed to | # of Copies | Distributed to | # of Copies |
| --- | --- | --- | --- |

This Procedural Bulletin is intended to provide a ready outline reference for performance of the assay. It is the obligation of every manufacturer of medical devices labeled FOR IN VITRO DIAGNOSTIC USE to provide a complete package insert in accordance with FDA labeling regulation (21 CFR 809.10). Prepared in accordance with the guidelines recommended by the Clinical and Laboratory Standards Institute, Wayne, PA 19087; CLSI Document GP2-A2.

IMCO provides CLSI procedures for your use.  The procedures are required to include the same information as listed in the package insert. Any modifications to this document are the sole responsibility of the Laboratory

CLIA Complexity: WAIVED

IMCO One Step HCG Urine Test is a rapid pregnancy test, which you can easily carry out yourself. It detects the presence of human chorionic gonadotropin (“HCG”), which appears in urine very early during pregnancy.

For in vitro self-testing use and Professional use only. For external use only.

#### HOW DOES IT WORK?

Human chorionic gonadotropin (hCG) is a hormone, produced by the developing placenta shortly after the conception and secreted into the urine. The pregnancy test contains antibodies which specifically react with this hormone.

When the strip is immersed into a urine specimen, capillary action carries the specimen to migrate along the membrane. When hCG in the sample reaches the Test Zone region of the membrane, it will form a colored line. Absence of this colored line suggests a negative result.

To serve as a procedure control, a colored line will appear at the Control Zone region, if the test has been performed properly.

Lab Name:      					Procedure #:

#### CONTENT OF THE TEST KIT

- One pouch containing a reaction strip and a desiccant.  The desiccant is for storage purposes only, and is not used in the test procedures.

- Leaflet with instructions for use.

#### WHAT ELSE DO YOU NEED?

- A clean, dry, plastic or glass container to collect the urine.

- Timer (watch or clock)

#### PRECAUTIONS

- This kit is for external use only. Do not swallow.

- Discard after first use. The test strip cannot be used more than once.

- Do not use test kit beyond expiry date.

- Do not use the kit if the pouch is punctured or not well sealed.

- Keep out of the reach of children.

#### STORAGE AND STABILITY

- Store at 4ºC to 30ºC in the sealed pouch up to the expiration date.

- Keep away from direct sunlight, moisture and heat.

- DO NOT FREEZE.

- Preferably open the pouch only shortly before the test.

#### SPECIMEN COLLECTION AND PREPARATION

WHEN TO COLLECT URINE FOR THE TEST ?

Any urine specimen is appropriate for Pregnancy Testing but the first morning urine specimen is optimal because of its highest concentration of HCG.

HOW TO COLLECT URINE?

#### Urine specimens may be collected in any clean, dry, plastic or glass container.

#### HOW TO DO THE TEST?

#### Allow the device and extraction reagents to equilibrate to room temperature (10ºC - 30ºC ) prior to testing.

- The test strip and urine have to be at room temperature (15-30°C) for testing.

- Remove the test strip from the sealed pouch.

- Immerse the strip into the urine with the arrow pointing towards the urine. Take the strip out after 3 seconds and lay the strip flat on a clean, dry, non-absorbent surface (such as the mouth of the urine container).

IMPORTANT： Do not allow the urine level to exceed the MAX (marker line), otherwise the test will not perform correctly.

- Read results in five minutes. Do not read results after more than 5 minutes.

Lab Name:      					Procedure #:

#### HOW TO READ THE RESULTS

Negative (not pregnant):

Only one color band appears, in the Control Zone. No apparent band on the Test Zone. This indicates that no pregnancy has been detected.

Positive (pregnant):

Distinct color bands appear in the Control and Test Zones. It indicates that you are pregnant. The color intensity of the test bands may vary since different stages of pregnancy have different concentrations of HCG hormone.

Invalid:

No visible band at all, or there is a visible band only in the test region and not in the control region. Repeat with a new test kit. If test still fails, please contact IMCO Technical Support at 1-844-369-2344 for further assistance.

NOTE: if the color in the Test Zone is weak, it is recommended that the test be repeated in 48 hours.

#### WHAT TO DO WHEN YOU KNOW THE RESULT

IF THE RESULT IS POSITIVE (TWO LINES)

Consult your physician. He should confirm your pregnancy after evaluating all clinical and laboratory findings. Indeed, in certain conditions, the test may give a false positive result. He will also give you further information and advice on your pregnancy.

See also “Limitations”.

Lab Name:      					Procedure #:

IF THE RESULT IS NEGATIVE (ONE LINE)

If you have reasons to believe that you are pregnant (e.g. no menstrual bleeding), you can repeat the test a few days later. If the test is still negative, consult your physician.

See also “Limitations”.

#### LIMITATIONS

- As it is with any diagnostic procedure, a confirmed pregnancy diagnosis should only be made by a physician after evaluating all clinical and laboratory findings.

- If a urine sample is too dilute (ie, low specific gravity) it may not contain a representative level of hCG. If pregnancy is still suspected, another urine specimen should be collected 48 hours later and tested.

- Low concentration of hCG in a very early pregnancy can give a negative result. In this case, another specimen should be obtained at least 48 hours later and tested.

- Elevated levels of hCG can be caused by a few conditions other than pregnancy. Therefore, the presence of hCG in urine specimen should not be used to diagnose pregnancy unless these conditions have been ruled out.

- A normal pregnancy cannot be distinguished from an ectopic pregnancy based on hCG levels alone. Also, spontaneous miscarriage may cause confusion in interpreting test results.

- Sterility treatments, based on hCG, may cause false results. Consult your physician.

#### EXPECTED RESULTS

Negative results are expected in healthy non-pregnant women and healthy men. Although the hCG levels in normal early pregnant women are variable, IMCO One Step Strip Urine HCG Test is capable of detecting pregnancy as early as 1 day after the first missed menses.

#### QUESTIONS & ANSWERS

- There is much difference between the control lines of two tests. Is this a concern? No. Variations in the color of the control band will not affect the test result.

- Can test results be interpreted after more than five minutes? No. Test results must be read in 5 minutes. Though a positive result should not change for several days, a negative result may change to a false positive within minutes after the end of the testing period, which would not be an accurate reading. It is always best to read the results at the 5 minute testing period and then discard the test to avoid confusion.

- A pink background color and vertical streaking appeared in the result area during the testing period. Is this a concern? No. Each urine sample will vary in its chemical makeup, as will the humidity of the air in testing chamber (room). Such variations in physical conditions can cause the vertical streaking and/or the pink-rose background color but will not affect the test results. As long as the control band appears within five minutes, the test is working properly.

Manufactured for:

Independent Medical Co-op Inc.

Daytona Beach, FL-32114

www.imcoinc.com

Technical Support:1-844-369-2344

Lab Name:      					Procedure #:

| LOG SHEET |
| --- |
| Record Built-in Procedural Controls on the first patient tested each day. |
|  | Date | Patient Name | Positive Procedural Control | Test Results Read at 5 minutes Do not read the test results after 5 (Five) minutes | Lot Number and Exp. Date | Technician |
| 1 |  |  |  |  |  |  |
| 2 |  |  |  |  |  |  |
| 3 |  |  |  |  |  |  |
| 4 |  |  |  |  |  |  |
| 5 |  |  |  |  |  |  |
| 6 |  |  |  |  |  |  |
| 7 |  |  |  |  |  |  |
| 8 |  |  |  |  |  |  |
| 9 |  |  |  |  |  |  |
| 10 |  |  |  |  |  |  |
| 11 |  |  |  |  |  |  |
| 12 |  |  |  |  |  |  |
| 13 |  |  |  |  |  |  |
| 14 |  |  |  |  |  |  |
| 15 |  |  |  |  |  |  |

Lab Name:      					Procedure #:

| LOG SHEET |
| --- |
|  | Date | External Positive Control Result | External Negative Control Result | Lot Number and Exp. Date | Technician |
| 1 |  |  |  |  |  |
| 2 |  |  |  |  |  |
| 3 |  |  |  |  |  |
| 4 |  |  |  |  |  |
| 5 |  |  |  |  |  |
| 6 |  |  |  |  |  |
| 7 |  |  |  |  |  |
| 8 |  |  |  |  |  |
| 9 |  |  |  |  |  |
| 10 |  |  |  |  |  |
| 11 |  |  |  |  |  |
| 12 |  |  |  |  |  |
| 13 |  |  |  |  |  |
| 14 |  |  |  |  |  |
| 15 |  |  |  |  |  |